STORZ BLIND CAP

Task Force Tips model #A01ST-PA lightweight, heat treated aluminum 5" Storz cap with suction gasket shall be provided. A 1/4" female NPT threaded hole shall be provided in the center of the cap. Cap is provided without locking lever. The unit shall be covered by a five-year warranty.