SPANNER & HYDRANT WRENCH SET

A Task Force Tips model #A3845 spanner & hydrant wrench set shall be provided. The set shall include two (2) lightweight aluminum universal spanner wrenches model # A3813 and one (1) single head adjustable hydrant wrench model # A3835. Spanner wrenches shall be made from lightweight cast aluminum alloy. Spanners shall fit most 1-1/4” through 4” couplings. Features shall include pin detail, window jimmy, gas cock slot, hammer head and hanger loop. Hydrant wrench shall have a manganese bronze head, plated steel handle, and have a high visibility grip and shall be for use on square or pentagon hydrant nuts. Compact spanner claw shall fit pin and rocker lug couplings.  Mounting bracket model # A3843 shall have quick, snap action releases and shall be included. The unit shall be covered by a five-year warranty.

Location of mounting bracket shall be: