30 DEGREE ELBOW

Task Force Tips model #AH5NJ-NJ-HP 30-degree high pressure elbow shall be provided. For corrosion resistance, the elbow shall be constructed of hardcoat anodized aluminum alloy, and include stainless steel ball bearings.

The elbow shall be marked “HIGH PRESSURE 600 PSI MAX” The elbow shall meet a 900 PSI hydrostatic test and comply with the current NFPA 1964 Standard. The unit shall have a unique, laser engraved serial number and be covered by a five-year warranty.

The elbow shall be configured with a 2-1/2" female NH swivel rocker lug coupling and a 2-1/2" male NH rigid thread.