MASTER STREAM NOZZLE

Task Force Tips model # M-RS4000-NN selectable flow master stream nozzle shall be provided. The nozzle shall be designed for use on monitors, ladder pipes, deluge guns and aerial platforms. For corrosion resistance the nozzle shall be constructed for lightweight hardcoat anodized aluminum.

The nozzle shall have a selectable flow rating of 1000 to 4000 LPM at a pressure of 7 BAR. The flow rating shall be user adjustable by depressing the outer baffle and selecting the desired flow. The various ratings shall be laser engraved on the baffle.

The following LPM flows are available

1000

1500

2000

2500

3000

4000

A UV resistant rubber bumper with integral teeth designed to produce a finger free fog pattern shall be included. A halo ring shall be included to assist with stream shape control. The nozzle shall be suitable for foam solution application and designed to accept the Task Force Tips FJ-LX-M low expansion air aspirating attachment. The nozzle shall be configured with a 3-1/2" female NH swivel rocker lug coupling.