PIERCING/DISTRIBUTOR NOZZLE KIT

Task Force Tips model # PA2 Transformer piercing and distributor nozzle kit shall be provided. The kit shall include a 12” flow tube with piercing tip, rotary valve, two 19” extension tubes, 3 port junction block, removable striking head, removable pistol grip, spinning distributor nozzle with 1-1/2” NH female adapter, and storage bag with carrying strap. The piercing nozzle tip shall be constructed from hardened stainless steel and be designed to penetrate common structures and other compartment areas where water and or foam need to be delivered. The distributor nozzle shall have a system of spinning heads for a wide, fully filled spray pattern. Each nozzle shall have a nominal flow capability of 150 GPM at 100 PSI. The inlet shall be a 1-1/2" female NH swivel coupling. The kit shall have a unique serial number and be covered by a five year warranty.