FLANGED MONITOR

Task Force Tips model # XX -AA flanged monitor shall be provided. The dual elbow waterway shall be adjustable to 90 degrees up and 45 degrees down relative to the flange inlet. For corrosion resistance and durability the unit shall be constructed from hardcoat anodized aluminum and have a powder coat interior and exterior finish, and be maintenance free.

The monitor shall have a 3" ANSI 150 flange inlet and a 2-1/2" male NH outlet.