1500 GPM FIXED LOCATION  MONITOR

Task Force Tips Typhoon, model # Y5-DL4A manually controlled monitor shall be provided. The Monitor shall operate with a hand wheel for rotation adjustment, and a hand wheel for elevation adjustment.

The monitor shall have the following capabilities:

Full horizontal rotation with 360 degree travel;

135 degrees of vertical travel from 90 degrees above horizontal to 45 degrees below horizontal

Field changeable rotation hard stops shall be provided at 45, 90 and/or 135 degrees left and right of center;

Field changeable hard stops in 10 degree increments left and/or right, and above and/or below horizontal;

Flow capability of 1500 GPM with 19 PSI of friction loss;

Maximum operating pressure of 200 PSI

For resistance to corrosion the monitor shall be constructed from hardcoat anodized aluminum with a silver powder coat interior and exterior finish. The discharge elbow shall include an integral stream straightener. A threaded port for an optional pressure gauge shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty.

The monitor shall be configured with a Task Force Tips code RLF threaded inlet to mate with Task Force Tips Extend-A-Gun RC3 telescoping waterway and 4" male BSP outlet.