1500 GPM FIXED LOCATION  MONITOR

Task Force Tips Typhoon, model # Y5-TP1A-Z manually controlled monitor shall be provided. The Monitor shall operate with a long tiller bar for elevation adjustment and  rotation adjustment and include locking knobs.

The monitor shall have the following capabilities:

Full horizontal rotation with 360 degree travel;

135 degrees of vertical travel from 90 degrees above horizontal to 45 degrees below horizontal

Field changeable rotation hard stops shall be provided at 45, 90 and/or 135 degrees left and right of center;

Field changeable hard stops in 10 degree increments left and/or right, and above and/or below horizontal;

Flow capability of 1500 GPM with 19 PSI of friction loss;

Maximum operating pressure of 200 PSI

For resistance to corrosion the monitor shall be constructed from hardcoat anodized aluminum with an American red powder coat interior and exterior finish. The discharge elbow shall include an integral stream straightener. A threaded port for an optional pressure gauge shall be provided. The unit shall have a unique serial number and be covered by a five-year warranty.

The monitor shall be configured with a Task Force Tips code RPF threaded inlet to mate with Task Force Tips Extend-A-Gun RC4 telescoping waterway and 3-1/2" male NH outlet.